BATTERIES: CHARGING, TESTING AND JUMPING

Procedure steps for properly charging a battery:

Steps:

- Make sure battery charger is unplugged.

- Connect charger to battery.

Make positive-to-positive connection.

Make negative-to-negative connection.

- Set charging rate, voltage and note the time.

- Plug in charger, turn charger on.

- To stop charging, turn charger off and unplug.

- Remove charging connections from battery

in reverse order.

Load testing battery procedure:

Steps:

- Ensure there is no load from carbon pile.

- Connect load tester to battery. (( Neg last)

- Apply load for no more than 10 seconds

- Record voltage reading.

- If voltage remains above 9.6volts,

Test again after 1 min.

- If voltage falls below 9.6volts, charge battery.

- Re-test, if voltage drops bellow

9.6 volts replace battery.

Procedure for properly jumping a battery:

Steps:

- Connect both positive terminals,

Together with jumper cables.

- Connect negative cable

To negative terminal of good battery,

Also known as donner vehicle’s battery.

- Connect negative cable to good known

Ground source away from battery

On vehicle being jumped.